Title: ADDSUB
By: V.N.Anirudh Oruganti
CSCE 212: Intro to Computer Architecture
Assignment: Project #1

Table of Contents

1.0 Project Description

The Project AddSub is a MIPS assembly code and uses only addition and subtraction to calculate the functions f=(ax+by), g=(cz+dw) and h=f/g. The MIPS assembly program code prompts the user for to input four positive integers a, b, c, and d as input parameters to which is later used to calculate the functions f,g and h. The parameters for x,y,z and w are the first, second, third, and fourth leftmost non-zero digits on the UofSC Student ID. My parameters for x,y,z and w are 8,4,3,5 respectively. After user inputs the parameters, program outputs the values of f and g in base 2 and 10 as well with the quotient and remainder of function h.

2.0 Program Design

As you could see in the flowchart(figure 1), it shows the program process from start to end. Firstly, it displays/outputs the title and instructions strings. Under the “.data” section, I had to name a massage and use “.asciiz” to print any kind of string message. To print the message in the console, we have to load registers $v0 with 4, $a0 with the name of the string, and use syscall to switch from user to kernel space. Secondly, to take inputs from the user for a,b,c,d as shown in the flowchart; similarly like to displaying a message we have to load registers $v0 with 5 and $a0 with a register (ex. $s0) to save user’s input, also use a syscall, and this process was repeated 3 more times to take values for b,c,d. Thirdly, four nested loops were used as you can see in the flowchart(figure 1) since we have to calculate four values for function f and g with exponents. Figure 2 flowchart shows the process I used to calculate the value for the number raised to powers. Firstly, I set $t0 to 1 since that’s going to be the counter for outer-loop and $t1 to x,y,z or w since that’s going be the power we are rising to(ex. a^t- $t1=t) and when $t0 and $t1 equals the loops is completed. Inside the outer-loop,$t2 which will be the counter for the inner loop that resets at the beginning of each loop and $t4 which will be set to $t5. Inner loop contains an two addition that adds one to the counter and the number in $t4 once every loop to $t5 until the condition is completed which mean that we multiplied a number times another number(ex. 7*7 or 8*5). Once the inner loop completes, the value in $t4 will be set to the value in $t5 and one is added to the counter. When this process is fully completed , the value in $t5 will be the calculated value for a^x or such and $t5 is added to a register of function’s f or g. The next process in the flowchart is to calculate the reminder and quotient for h when the function h=f/g. To do this I used a loop shown in figure 3 flowchart which has a count that will be the quotient and remainder will be the value in $t0. The way the division is done in my loop is when the number of times g is subtracted from f will be the quotient and when g is greater than f, which mean that leftover f is the reminder. Then proper values in the temporary register to a location in s registers. All the values are outputted in the same manner we did at first but 1 had to be loaded in $v0 to show an a integers or 35 for base-2 value.
Figure 1

Figure 3
Figure 2

3.0 Symbol Table
Register $	Description
t0	Used as a for Counter for loops and temporary value for f in the last loop
t1	Number of loops parameter
t2	Used as a Counter for loops
t3	Number of loops parameter
t4	Used to addition for $t5 aka help calculate a^x
t5	Used to calculate a^x
s0	User’s a value
s1	User’s b value
s2	User’s c value
s3	User’s d value
s4	Value for function f
s5	Value for function g
s6	Reminder for h
s7	Quotient for h
v0	Used for type of output and to take input
a0	Used to prompt with a message

Label	Description
Title	“MY ID: T84354488”
HQ	"\nh_quotient = "
HR	"\nh_remainder = "
f10	"\nf_ten = "
f2	"\nf_two = "
g10	"\ng_ten = "
g2	"\ng_two = "
Instructions	"\nEnter 4 positive integers for a,b,c,d respectively\n"
Nestedloop(1-4)	This is the start name of outer loop that is a nested loop that calculates a^x and such
EndofNestedloop(1-4)	This is the end name of outer loop that is a nested loop that calculates a^x and such
InnerNestedloop(1-4)	This is the start name of inner loop that is a nested loop that calculates a*a and such
EndofInnerNestedloop(1-4)	This is the end name of inner loop that is a nested loop that calculates a*a and such
startloop	This is start name of a loop that calculates h
endloop	This is end name of a loop that calculates h